## Slide 1
Control unit
Instruction sequencing
Methods by which instructions are selected for execution or how control of processor transfers from one instruction to other
Instruction interpretation
How a control unit interprets an instruction to determine the control signals to be issued?
CU
Data processing unit (DPU)
Input data
Output data
Cin
Cin
Cout
Cout
Digital system is separated into two parts: CU and DPU
CU: Issue control signal or instruction to DPU
Fetch instruction from memory
Interpret instruction to determine the control signals to be sent to DPU
DPU: Performs certain operations on data
Control signal: Selects the function to be performed at specific time
Route the data through the appropriate functional units
Cout: Directly control the operation of DPU
Cin : Enable the data being processed to influence CU
Allowing data dependent decisions to be made
Indicate the occurrence of unusual condition such as errors like overflow in DPU
Cout : Transmitted to other CUs, may indicate status conditions such as “busy” or “operation completed”
Cin : Receives from other CUs e.g. from a supervisor or controller, typically include start signal, stop signal, timing
information

## Slide 2
T1
T6
T5
ADD
BR
Zin
Example 1: Let control signal Zin is required to be activated at T1 time instant for all instructions, during T6 for ADD instruction, during T5 for conditional branch instruction etc.
Zin = T1+(ADD)T6 + (BR) T5+….
Example 2: Suppose C5 control signal is required in the fetch cycle of all the instructions at time instant T2, during the execution of instruction I1 at time instant T4, during the execution of instruction I2, I3 at time instant T6. P is 0 for fetch and 1 for execute.
C5 = P T2 + P(I1 T4 + I2 T6 + I3 T6)
Design methods of hardwired CU
State table method: Behaviour required of a CU , like that of any finite state sequential machine, can be represented by a state table, Cin and Cout determine the input and output variables of CU
States | I1 | I2 |  |  |  | Im
S1 | S11Z11 | S12Z12 |  |  |  | S1mZ1m
S2 | S21Z21 | S22Z22 |  |  |  | S2mZ2m
Sn | Sn1Zn1 | Sn2Zn2 |  |  |  | SnmZnm
{Si}  Set of internal states of the machine as defined by the rows of the state table
Internal state  Determined by the information stored in the unit at discrete points of time (clock time)
Column corresponds to the set of external signal to CU i.e. Cin
SijZij  Entry in row Si and column Ij
Zij: Denotes the set of output signal from Cout that are activated due to the application of Ij to control unit when it is in state Si
Sij: Denotes the next state of CU

## Slide 3
CU state Si
.
.
.
Zij
Ij
Next state Sij
Start
A0, Q0, count n
AA-M
AA+M
ashr
Q0Q-1
S1, {C9, C10}
S4, {C0, C1}
S2, {C2, C3, C4}
S3, {C2, C3, C4, C5}
01
10
00,11
Disadvantage: Size of state table and amount of computation increase with the number of state and input combinations
Delay element
.
.
.
{C1j}
Start(t1)
Delay element
.
.
.
{C2j}
Start(t2)
.
.
.
{C3j}
Start(t3)
2. Delay element method: Uses clocked delay element for control signal timing
Consider the problem of generating the following sequence of control signals at time t1, t2, …tn using hardwired CU
t1: Activate {C1j};
t2: Activate {C2j};
.
.
.
tn: Activate {Cnj};

## Slide 4
Output control
pulse
Input control
pulse
Clock
Q
Input control
pulse
Clock
Output control
pulse
D
Q
0
clk
Synchronous delay element for CU design
Begin
{C1j}
{C2j}
{C3j}
{C4j}
{C5j}
{C6j}
is x1=1
is x2=1
yes
yes
no
no
DE
Begin
{C2j}
DE
DE
{C1j}
x1
x1′
x1′
x2
x2′
.
.
.
{C3j}
.
.
.
{C4j}
.
.
.
{C5j}
.
.
.
{C6j}
Flow chart showing the control signals to be activated
k lines in the flow chart that merges to a common line are transformed into a k input OR gate
Implementation of decision box using AND gate

## Slide 5
S
1
R
0
FF
Mod-k counter
Begin
End
Clock
Reset
Count enable
Reset
1/k decoder
. . .
. . .
1
2
k
3. Sequence counter method
Begin=1, End=0, FF output = 1, Count enable = clock, counter goes on counting k clock pulses, for each count value one of the decoder output is high
Counter count value = i at ith clock pulse, i phase signal at the decoder output is activated, i activates a set of control signals in step i of every instruction cycle
A pulse at the end line disconnects clock and resets the counter
Mod-16 sequence counter
Reset
4 to 16 decoder
. . .
0
1
15
Clock

## Slide 6
Transfer PC to MAR
Fetch instruction from MM
PCPC+1
Decode instruction
Transfer operand address to MAR
Fetch operand(s) from MM
Perform operation specified by the instruction
CPU behaviour represented as
a single closed loop
Each pass through the loop constitutes an instruction cycle
Assuming that each step can be performed in an appropriately chosen clock period
Modulo-6 counter may be used to build this
Each signal i activates some set of control lines in step i of every instruction cycle
Operations performed in step i can be varied depending upon the certain control signals and condition variables applied to CU through Cin, Cin
Cin = {Cin, Cin}
A logic circuit is needed to combine Cin with the timing signal {i} generated by the sequence counter
Mod-k sequence counter
Begin
End
Clock
Reset
1
2
k
. . .
Mod-k sequence counter
Logic circuit
. . .
.
.
.
.
.
.
1
2
k
Cin
Cout
At ith clock pulse i output of sequence counter is activated to generate the desired control signals at step i of every instruction cycle
If it is required to vary the operations performed in step i depending on certain control signals or condition variables applied to the CU (Cin = {Cin, Cin}), a logic circuit combines Cin with the timing signal {i} generated by the sequence counter.

## Slide 7
Disadvantage of hardwired CU
Hardwired CU becomes complicated in case of large number of instructions and control lines, costly, difficult to design
Inherently inflexible if it is required to correct design errors or modify instruction set, needs redesign of CU
Microprogrammed CU
Instruction/Operation: Instruction is executed to do operation. For example, ADD R1,X is an instruction. It does add operation. It adds the content of register R1 and the content of the memory location X.
Microinstruction/Micro operation:
Add operation in the instruction ADD R1, X is divided into a few micro operation as follows
MAR  PC
MDR  (M(MAR)), PC  PC+1
IR  MDR
Control block  IR(opcode)
MAR  IR(address) ----address = X
MDR  operand = data at X
R1  R1 + (MDR)
To execute each micro operation a set of control signal is required to activate
This set of control signal is activated by microinstruction
Hence to execute each micro operation, one microinstruction is required. For example, add operation in ADD R1, X is divided into 7 micro operations, and so 7 microinstructions are required to execute 7 micro operations.

## Slide 8
Microprogram, microinstruction, control memory (CM)
Microprogram = a sequence of microinstructions
ADD R1, X  instruction that does addition operation, divided into 7 micro operations which needs 7 sets of control signal for execution and hence 7 microinstructions.
So the microprogram corresponding to the instruction ADD R1, X contains 7 microinstructions. This microprogram resides in CM with starting address say P.
I1
I2
I3
I4
I5
I6
I7
CU
CM
P
ADD R1,X
CU receives ADD R1, X;
CU computes the starting address of the corresponding microprogram in CM i.e. P from the opcode of this instruction, executes all the microinstructions in sequence from address P.
The execution of 7 microinstructions activates 7 sets of control signals to execute 7 micro operations
Format of microinstruction
Control field
Address field
Activates control signal to execute micro operation
Address of the next microinstruction to be executed
CM: ROM if the instruction set of a processor is permanent
WCM (Writeable CM) allows to change the content of CM dynamically

## Slide 9
Wilkies design
CMAR
1/8 decoder
S
External condition
External address = P
C1
C2
C4
C3
C6
C8
C5
C7
a1
a2
a0
Control memory
Each row indicate one microinstruction
Top most horizontal line represents the microinstruction at address 000
External address source stores 000 in CMAR
Microinstruction at address 000 in CM is selected , control lines C1, C3, C6, C7 are activated
Address field of the microinstruction at location 000 in CM contains 001 which is the address of the next microinstruction
 | Control field | Address field
I1 | C1, C3, C6, C7 | 001
I2 | C2, C4 | 010
I3 | C3 | 011
I4 | C2, C5, C6, C8 | 111
I5 | C1, C7 | 101
I6 | C3, C4 | 110
I7 | C2, C6 | 111
I8 | C8 | 010
External condition: Any CU must be able to give response to external signals or conditions
Switch S is controlled by an external condition FF
Address field of 4th microinstruction contains 111 whereas the address field corresponding to switch S contains 100. So depending upon the external condition either microinstruction at location 111 or 100 in CM is executed.

## Slide 10
Example:
Operation LOAD R i.e. load the register R. Suppose
the register R can be loaded from four different sources
R  X0, control signal C0 is activated
R  X1, control signal C1 is activated
R  X2, control signal C2 is activated
R  X3, control signal C3 is activated
Register R
X0
X1
X2
X3
C3
C2
C1
C0
C0
C1
C2
C3
 Control field 
0 0 0 R  X0
0 1 0 0 R  X1
0 0 1 0 R  X2
0 0 0 1 R  X3
0 0 0 0 NOP
Five micro operations
Horizontal microinstruction
Vertical microinstruction
K0
K1
K2
 Control field 
3 to 8 decoder
C0
C1
C2
C3
C7
. . .
C0 = 1 when K0K1K2 = 001
C1 = 1 when K0K1K2 = 010
C2 = 1 when K0K1K2 = 011
C3 = 1 when K0K1K2 = 100
Advantage of vertical microinstruction format over horizontal microinstruction format
Reduces length of control field by 1 bit at the cost of an extra decoder
Short format
Needs encoding
N independent control signals for N independent micro operations can be encoded in a control field of log2(N+1) bits
Fig. Horizontal and vertical microinstruction format

## Slide 11
Parallelism in microinstruction
One instruction executes one operation. Let this operation is divided into N micro operations. So N number of microinstructions are required to generate N set of control signals. As with the number of micro operation number of microinstruction increases, size of the microprogram also increases which needs more storage space in CM.
Parallelism in microinstructions is used to reduce the number of microinstructions and hence to reduce the size of CM.
Definition: In microprogramming level independent micro operations are available and executed in parallel. Hence one microinstruction can specify control signals that are required to execute multiple independent micro operations.
Example of dependent micro operation: AC0, ACAC-DR
Example of independent micro operation: MDR  (M(MAR)), PC  PC+1
Control field
Address field
20 bits
9 bits
11 bits
Address field
9 bits
3 bits
3 bits
3 bits
CM: Number of memory locations = 211
Each memory location contains 20 bits microinstruction
Size of CM = 211 x 20 bits
9 bits control field is divided in 3 field that is 3 sets of control signals for 3 independent micro operations can be activated by a single microinstruction.
Degree of parallelism = 3

## Slide 12
F1=F2=F3=000 signifies NOP |  | 
F1 = 001  AC  AC+DR F1 = 010  AC  0 F1 = 011  AC  AC+1 . . . | F2 = 001  AC  AC-DR F2 = 010  AC OR DR . . . | F3 = 001  AC  ACDR F3 = 010  AC AC′ F3 = 011  PC  MAR . . .
Let us consider two micro operations as PC  MAR and AC  AC+DR. These two micro operations are independent. So the control signals that are required to activate for the execution of the two micro operations can be specified in a single microinstruction.
Address field
001
000
011
Control field
Example:
Total number of micro operation = 46
Degree of parallelism = 2
What is the size of two subfields in 9 bits control field of microinstruction?
24 + 25 = 16 + 32 = 48 = 46+2
NOP

## Slide 13
Control memory optimization
Monophase: So far we have assumed that each microinstruction generates a set of control signals which are active for the duration of the microinstruction execution cycle
Clock period = microinstruction cycle period
Polyphase: The number of microinstructions needed to specify a particular operation can often be reduced by dividing the microinstruction cycle into several sequential phases. Each control signal is typically remains active during only one of the phases. This phase permits a single microinstruction to specify a sequence of micro operations.
Example: Micro operation , R  f(R1, R2)
Transfers content of R1 and R2 into the input of f unit
f unit
Register
R
R1
R2
CM
W
H
1
2
3
Transfers content of R1 and R2 into the input of f unit
Store the result generated by f unit in a register
Transfers content of register into R
Microinstruction cycle
Microcode compaction
Reduce H by merging two or more micro operations into a single microinstruction

## Slide 14
Basic principle of merging
m1 : R2  F(R1)
m2 : R3  F(R2)
m3 : R4  F(R3)
m1 and m2 have direct data dependency
m1 and m3 have indirect data dependency
m2 and m3 have direct data dependency
m1, m2, m3 can’t be executed in parallel, can never be placed in the same monophase microinstruction, may appear in different phases of the same polyphase microinstruction
Data dependent micro operations can be executed sequentially in the proper time sequence within a single microinstruction cycle
Such data dependent micro operations are called weakly data dependent
Example: Microinstruction cycle is divided into 3 subphases |  |  |  | 
Microinstruction before compaction |  |  |  | Microinstruction after compaction
Name | Micro operation | Phase used | Resource used | 
m1 m2 m3 m4 m5 m6 m7 | RLEFT  AC RRIGHT  1 ROUT  RLEFT+RRIGHT MARRIGHTSHIFT(ROUT) M(MAR)  MDR RLEFT1 RRIGHT  R0 | 1 1 2 3 2 1 1 | Adder Shifter Bus | I1 = {m1} I1 = {m1, m2} I1 = {m1, m2, m3} I1 = {m1, m2, m3, m4} I2={m5} I2={m5, m6} I2={m5, m6, m7}
H = 2

## Slide 15
Microinstruction after compaction
m1, m2 are independent and so can be executed in the same phase 1 and can be included in the same microinstruction I1
m1, m2, m3 are dependent but m3 needs different phase 2, so m3 can be included in I1 (due to weak data dependency)
m3 and m4 are dependent but they need different phase and resource, hence m4 can be included in I1
m4 and m5 are strongly data dependent, m5 needs 2 for execution, so need to be placed in different microinstruction I2
m1 and m6, m2 and m7 are strongly data dependent. So m6 and m7 can’t be placed in I1. But m6 and m7 are independent on m5 and so can be placed in I2
Example: Microinstruction cycle is divided into 3 sbphases |  |  |  | 
Microinstruction before compaction |  |  |  | Microinstruction after compaction
Name | Micro operation | Phase used | Resource used | 
m1 m2 m3 m4 m5 | A  R1 C  A+R2 R3  D R6R6+1 R7  R3 OR R6 | 1 2 2 2 2 | Adder Adder ALU | I1 = {m1} I2 = {m2} I1 = {m1, m3} I1 = {m1, m3, m4} I2={m2, m5}
m1 and m2 are strongly data dependent
m2 and m4 are resource dependent, both needs 2
m4 and m5 are data dependent, both needs 2
As m4 needs adder like m2
H = 2

## Slide 16
Minimizing W
Objective is to derive a format of the microinstruction control field such that the total number of bits in the control field is a minimum i.e. we want a control field encoding method that uses as few bits as possible
Steps of operation
Determine the set of maximal compatibility class (MCC)
Determine all minimal set of MCCs that include each control signal. Each of these sets is called minimal MCC cover
Inspect each minimal MCC cover {Ci} in turn and determine all way of including each control signal in exactly one subset of some Ci.
Compatibility class
Ci = control signal, Ij = microinstruction
Ci ϵ Ij  Ci is activated by Ij
Control signals C1 and C2 are compatible if C1 ϵ Ij but C2 ϵ Ij and vice versa
Maximal compatibility class : Defined as compatibility classes to which no control signal can be added without introducing a pair of incompatible control signals
Example | 
Microinstruction | Control signals
I1 I2 I3 I4 | a, b, c, g a, c, e, h a, d, f b, c, f
Step-1: Determine the set of MCCs
First determine all compatibility classes containing two control signals
Second determine all compatibility classes containing three control signals
Process terminates when no new compatibility classes can be formed
S1: a b c d e f g h
S2: bd be bh cd de dg dh ef eg fg fh gh
S3: bde bdh deg dgh efg fgh
Rule for forming Si+1 from Si:
Add a new control signal to a, say {a,b}
Pair {a,b} is not compatible so check for {a,c} and so on

## Slide 17
Step-2: Determination of all minimal set of MCCs that include each control signal. Each of these sets is called minimal MCC cover
Uses cover table that contains a row for each MCC (Ci) and column for each control signal (Cj)
X is placed at the intersection of row Ci and column Cj if Cj ϵ Ci i.e. Ci covers Cj.
 | a | b | c | d | e | f | g | h
C1 = a | X |  |  |  |  |  |  | 
C2=cd |  |  | X | X |  |  |  | 
C3=bde |  | X |  | X | X |  |  | 
C4=bdh |  | X |  | X |  |  |  | X
C5=deg |  |  |  | X | X |  | X | 
C6=dgh |  |  |  | X |  |  | X | X
C7=efg |  |  |  |  | X | X | X | 
C8=fgh |  |  |  |  |  | X | X | X
MCC Ci
Control
Signal Cj
Certain rows and columns can be deleted from the cover table to simplify determination of the minimal MCC covers
1. Column Cj contains only one X, which occurs in row Ci, Ci is said to be an essential MCC and must appear in every minimal MCC cover, since it only covers Cj
Example: Column a and column c contain only one X. So C1 and C2 are two essential MCC and must appear in every minimal MCC cover since C1 is only MCC that covers the control signal a and C2 is only MCC that covers the control signal c
2. All rows corresponding to essential MCCs can be deleted from the cover table and all columns with X in essential rows can be deleted
Hence deletes row C1, C2 and columns a, c, d.
3. If the cover table contains two identical columns then all but one of these columns can be deleted.
Example: there is no identical columns

## Slide 18
4. Column Ci is said to dominate column Cj if Ci contains an X in every row where Cj contains an X and Ci contains more X than Cj
The dominating column can be deleted as every MCC that covers Cj automatically covers Ci
Example: d dominates b and c while g dominates f , hence deletes column g
5. Row Ci is said to dominate row Cj if Ci contains an X in every columns where Cj contains an X and Ci contains more X than Cj
In this case the dominating row Cj can be deleted, since Ci covers all the control signals that are covered by Cj
Example: There is no such dominating row.
 | b | e | f | h
C3=bde | X | X |  | 
C4=bdh | X |  |  | X
C5=deg |  | X |  | 
C6=dgh |  |  |  | X
C7=efg |  | X | X | 
C8=fgh |  |  | X | X
MCC Ci
Control
Signal Cj
Reduced cover table
Step-3: Inspect each minimal MCC cover {Ci} in turn and determine all ways of including each control signal in exactly one subset of some Ci
The minimal cover for this table contains two MCCs, possible choices are {C3, C8} and {C4, C7}
Combining these with essential MCCs C1 and C2 the desired MCC solutions are {C1, C2, C3, C8} and {C1, C2, C4, C7}.
Consider one of the two minimal MCC, say {C1, C2, C3, C8}.
There is only one way to cover a (by C1), b (by C3), c (by C2), e (by C3), f,g,h (by C8).
There is two way to cover d (by C2 and C3).

## Slide 19
If we decide to cover d by C2 then delete d from C3 to obtain the partition {a, cd, be, fgh}.
F1, F2, F3, F4 are the four subfields in microinstruction control
W = width of the control field = 7 bits
X
XX
XX
XX
0 NOP
1 a
Decoder 1
Decoder 2
Decoder 3
F1=a=C1
F2=cd=C2
F3=be=C3
F4=fgh=C8
Decoder 1 | Decoder 2 | Decoder 3
00  NOP 01  d 10  c | 00  NOP 01  b 10  e | 00  NOP 01  f 10  g 11  h
X
XX
XX
X
0 NOP
1 a
Decoder 1
Decoder 2
F1=a=C1
F2=c=C2
F3=bde=C3
F4=fgh=C8
Decoder 1 | Decoder 2
00  NOP 01  b 10  d 11  e | 00  NOP 01  f 10  g 11  h
If we want to cover d by C3 then delete d from C2 to obtain the partition {a, c, bde, fgh}
W = 6 bits, number of decoder reduces
Totally horizontal microinstruction format needs 8 bits in control field for 8 control signals without the use of any decoder. So vertical format needs 6 bits and horizontal format needs 8 bits in the control field.