## Slide 1
Instruction sets
Specify an operation to be carried out or set of operands or data to be used
Operation specified in opcode field of the instruction
Operand field includes input data and results that are produced
Operand field of the instruction contains addresses of storage locations in main memory or in the processor
Opcode
. . .
Operands
2
3
n
1
Instruction format
n-operand format
To reduce instruction size and thereby reduce program storage space it is common to specify only m<n operands explicitly in the instruction, remaining operands are implicit
Explicit address fields usually refer to main memory implicit ones refer to registers
If m is the maximum number of explicit main memory addresses allowed in any processor instruction, the processor may be called an m-address machine
Implicit input operands must be placed in locations known to the processor before the instruction that refers to them is executed
Addressing modes
Operand field of an instruction contains a piece of data X
To execute instruction processor requires the current value of X, this value can be specified in several ways, termed addressing modes
Add r1, r2: r1r1+r2
Add r1, M(X): r1r1+M(X)
MOV A, M(X): X is explicit
MOV A, B: B is implicit

## Slide 2
Immediate addressing: X (Operand) is constant, its value can be placed in the instruction operand field
Direct addressing: X (Operand) is variable, then operand field X contains address of the memory location of the operand. Requires one fetch operation for getting the operand.
Indirect addressing: Instruction operand field contains the address W of a storage location which in turn contains address X of the desired operand. By changing the content of W, address of the operand value required by the instruction is effectively changed
Requires two fetch operation for getting the operand.
LOADI
999
999
Main memory
AC
LOAD
X
AC
X
W
999
Main memory
LOADN
W
AC
X
W
X
Immediate
Direct
Indirect
Absolute addressing: Direct addressing needs the complete operand address
Partial addressing information is included in the instruction, so the complete (absolute) operand address must be constructed by the processor
Relative addressing: Operand field contains a relative address or displacement D
Absolute or effective address (A) = Single address register from a set of general purpose registers associated with the operand (R) + Displacement (D)
Why relative addressing:
Instruction length is reduced as all the address information need not be included in the instructions
By changing the content of R, processor can change the absolute addresses referred to by a block (B) of instructions
Permits the processor to move (relocate) the entire block B from one region of memory to another without invalidating the addresses in B
When used in this way, R may be referred to as a base register and its content as a base address

## Slide 3
R can be used for storing indices to facilitate the processing of indexed data, in this role, R is called index register
Indexed items X(0), X(1),…X(i) are stored in consecutive addresses in main memory. Instruction address field contains D the address of the first item X(0) while the index register R contains the index i. Address of item X(i) is D+R.
By changing the content of the index register, a single instruction can be made to refer to any item X(i) in the given data list.
Disadvantage: Needs extra logic circuits and extra processing time for address computation
Autoindexing: Indexed items are frequently accessed sequentially so that a reference to X(k) stored in memory location A is immediately followed by a reference to X(k+1) or X(k-1) stored in location A+1 and A-1 respectively.
To facilitate stepping through a sequence of items in this manner, addressing modes that automatically increment or decrement an address can be defined.
Example: -(A3)  Predecrement: indicates the content of A3 should be decremented automatically before the instruction is executed
(A3)+  Postincrement: indicates the content of A3 should be incremented automatically after the execution of the instruction
Stack addressing: Part of main memory M used as a pushdown stack
Logical sequence of items which are accessible from only one end referred to as the top of the stack
PUSH operation: Write, stores item at the top of the stack
POP operation: Read, removes item stored at the top of the stack
Changes the position of the stack top by the length of the operand pushed or popped
Stack pointer (SP): Address register
Stores the address of the last operand placed in the stack
Contains new stack top after PUSH/POP operation

## Slide 4
Number of addresses
Three address machine: ADD Z,X,Y; ZX+Y; add the contents of the memory location X and Y, place the result in location Z
Two address machine: ADD X,Y; XX+Y; accumulator may be used to store the result, in that case ACX+Y;
One address machine: ADD X; unspecified operands are assumed to be stored in fixed locations, commonly in a processor register AC; ACAC+X
Zero address machine: ADD; causes the two top operands X and Y to be removed from the stack and added; store the result at the top of the stack
One address machine | 
LOAD A MULTIPLY B STORE T LOAD C MULTIPLY C ADD T STORE X | ACA ACAC x B M(T)AC ACC ACAC x C ACAC +T M(X)AC
Two address machine | 
MOVE T,A MULTIPLY T,B MOVE X,C MULTIPLY X,C ADD X,T | T A TT x B XC XX x C XX+T
Three address machine | 
MULTIPLY T,A,B MULTIPLY X,C,C ADD X,X,T | T A x B XC x C XX+T
Zero address machine | 
PUSH A PUSH B MULTIPLY PUSH C PUSH C MULTIPLY ADD POP X | Transfer A to top of stack Transfer B to top of stack Remove A, B from top of the stack and replace by A x B Transfer C to top of stack Transfer second copy of C to top of stack Remove C, C from top of the stack and replace by C x C Remove C x C and A x B from stack and replace by their sum Transfer result from top of stack to X
A
A
B
AxB
AxB
C
AxB
C
C
AxB
CxC
AxB+CxC

## Slide 5
Opcodes
In most computers, the opcode field is a fixed length field of k-bit within each instruction
Permits up to 2k distinct operations
Some addressing information may also be included in the opcode field, for example, the addresses of processor registers used to store operands
Programs occupy a considerable amount of valuable storage space, so objective is to reduce their length as much as possible
Frequency with which operand addresses occur can not be reasonably determined; all may be assumed to have equal
probability
Frequency with which specific instruction types occur can be determined but it depends on the instruction mixes
Attempt can be made to control the opcode length depending upon their probability of occurrence
Fixed opcode length: Easy to decode and store
Variable opcode length: Significant storage saving can result
Opcode having higher probability of occurrence in average application programs are encoded with fewer bits
Variable length opcode based on instruction occurrence probabilities |  | 
Instruction | Probability of occurrence | Opcode Ci
I1 I2 I3 I4 I5 | 0.5 0.3 0.08 0.06 0.06 | 1 01 000 0011 0010
Fixed length opcode needs 3-bit per opcode
Variable length opcode needs average number of bits per instruction =
Choose each opcode carefully for unique decoding
% of saving =

## Slide 6
Huffman’s method of optimal coding scheme |  |  |  |  |  |  |  | 
 | L1 |  | L2 |  | L3 |  | L4 | 
pi,1 pi,2 pi,3 pi,4 pi,5 | 0.5 0.3 0.08 0.06 0.06 | 1 01 000 0011 0010 | 0.5 0.3 0.12 0.08 | 1 01 001 000 | 0.5 0.3 0.2 | 1 01 00 | 0.5 0.5 | 1 0
A systematic method of constructing codes to minimize average opcode length
Opcode decoding: Scan any given instruction from left to right
An instruction beginning with 0100… must be of type I2
Instruction types: What type of instructions should be included in a general purpose processor’s instruction set
Requirement to be satisfied by an instruction set
It should be complete in the sense that one should be able to construct a machine language program to evaluate any function that is computable using a reasonable amount of memory space
Instruction set should be efficient in that frequently required functions can be performed rapidly using relatively few instructions
It should be regular i.e. it should contain expected opcodes and addressing modes, e.g. if there is left shift, there should be a right shift
To reduce both hardware and software design cost, the instructions may be required to be compatible with those of existing machines, e.g., previous members of the same computer family
A "computer family" refers to a group of computers sharing similar architecture, design, and core components, allowing
them to run the same software, like the IBM PC family

## Slide 7
Instructions are conveniently divided into 5 major groups
1) Arithmetic instruction: Perform operations on numerical data
Example: Add, Subtract, Multiply, Divide, Absolute (replace operand by its absolute value), Negate (change sign of operand), increment, decrement
2) Logical instruction: Include Boolean or other nonnumerical operations
Example: AND, OR, NOT, EX-OR, Shift, Rotate, Convert (change data format from binary to decimal)
3) Data transfer instruction: Cause information to be copied from one location to another
Example: Move, Store, Load, Exchange (swap source and destination content), Clear (transfer word of 0’s to destination), Set (transfer word of 1’s to destination), Push, Pop
4) Program control instruction: Change the sequence in which programs are executed
Example: Jump, Jumpconditional, Jump to subroutine, Return, Execute (fetch operand from a specified location and execute instruction), Skip (increment PC to skip next instruction), Test (test specified condition based on outcome), Compare
5) I-O instruction: Cause information to be transferred between the processor or its main memory and external IO devices
Example: Input, Output, Start IO (transfer instruction to IOP to initiate IO operation), Test IO (transfer status information from IO system to specified destination), Halt IO (transfer instruction to IOP to terminate IO operation)
Note: A function returns a value to the calling code, while a subroutine performs a task without returning a specific value.

## Slide 8
Reduced instruction set computer (RISC)
Developed at IBM in the mid 1970s
Relatively few instruction types and addressing modes
Fixed and easily decoded instruction format
Fast single cycle instruction execution
Hardware rather than micro program control
Memory access limited mainly to load and store instructions
Use of compilers to optimize object code performance
Most RISC instructions involve only register-to-register operations that are internal to the CPU
Reduces execution time to single cycle
Allows CPU cycle time and hardware complexity to be minimized
Complex instructions are implemented by routines due to the unavailability of the complex instructions in the instruction set
Complex instruction set computer (CISC)
A large number of instructions typically from 100 to 250 instructions
Some instructions that perform specialized task are used infrequently
A large variety of addressing modes from 5 to 20
Variable length instruction format

## Slide 9
Execution of instructions
Instructions are executed in instruction cycle
Instruction cycle has two parts, fetch and execute
Fetch cycle: PC contains the address of the next instruction to be executed
MDR
MAR
PC
IR
Control block
MAR
Opcode
Operand
Main memory
MAR  PC
MDR  (M(MAR))
IRMDR
MARIR(operand), control block  IR(opcode)
Control block starts to decode the instruction
CPU switches from fetch to execute cycle
Execution cycle
Execution of an instruction involves execution of a set of micro operations
Set of micro operations and their sequencing depends on the opcode and operand data type
Control block generates the sequence of control signals necessary to execute each of the micro operations during decoding
Example |  | 
Instruction | Operation | Micro operations
MOVE R1 LOAD X ADD X | ACR1 ACM(X) ACAC+M(X) | DRR1, ACDR ARDR (operand part), Read M, DRMDR, AC  DR ARDR(operand), Read M, DRMDR, ACAC+DR

## Slide 10
Arithmetic instruction implementation
Addition and subtraction with signed-magnitude data |  |  |  | 
Operations | Add magnitudes | Subtract magnitude |  | 
 |  | When A>B | When A<B | When A=B
(+A)+(+B) | +(A+B) |  |  | 
(+A)+(-B) |  | +(A-B) | -(B-A) | +(A-B)
(-A)+(+B) |  | -(A-B) | +(B-A) | +(A-B)
(-A)+(-B) | -(A+B) |  |  | 
(+A)-(+B) |  | +(A-B) | -(B-A) | +(A-B)
(+A)-(-B) | +(A+B) |  |  | 
(-A)-(+B) | -(A+B) |  |  | 
(-A)-(-B) |  | -(A-B) | +(B-A) | +(A-B)
Add the two integer
and attach the sign of A
Subtract B from A
and attach the sign of A
Subtract A from B
and attach the sign of B
Two equal numbers are subtracted, result +0 not -0
Hardware implementation
A and B be two registers to hold the magnitude of the numbers
As and Bs are two flip-flops to hold the sign of A and B
Result of the operation may be transferred to a third register or into A and As
A and As together form an accumulator register
Parallel adder performs A+B
Comparator to compare the magnitudes of A and B
Two parallel subtractor circuit to compute A-B and B-A
XOR gate to find sign relationship with As and Bs
Addition
As=Bs, Addition and As ≠ Bs, Subtraction
Subtraction
As=Bs, Subtraction and As ≠ Bs, Addition

## Slide 11
B register
A register
Complementer
Parallel adder
Bs
As
AVF
=E
Mode control
M, 0(1)
Input carry 0(1)
Output
carry
B
E
B(B′)
A+B/(A+B′+1)
A
Load sum
Procedure to minimize hardware equipment
Subtraction can be done using complement and addition
Result of comparison can be determined from the end carry after the subtraction
Use of 2’s complement for subtraction and comparison is an efficient procedure as it requires only one adder and one complementer
Subtraction can be done by adding A with 2’s complement of B
Output carry is transferred to E for comparison (A>B, A<B, A=B)
AVF holds overflow bit when A and B are added
Complementer consists of XOR gates
Parallel adder consists of full adder
Addition M=0, input carry = 0, adder output = A+B
Subtraction M=1, 1’s complement of B is applied to the adder, input carry = 1, output = A+B′+1=A-B
Minuend in A
Subtrahend in B
AsBs
EAA+B′+1
AVF0
E
AA′
AA+1
AsAs′
As0
A
END
Result is in A
and As
Augend in A
Addend in B
AsBs
EAA+B
AVFE
Add operation
Subtract operation
=1, addition
As≠Bs
=0,
As=Bs
0,A<B
1,A≥B
=0
≠0
As≠Bs
=1,
As≠Bs
=0, subtraction
As=Bs

## Slide 12
Addition and subtraction with signed 2’s complement
Left most bit of a number represent the sign bit
Negative number is represented in 2’s complement form
Overflow
Result of addition of two n-bit number has n+1 number of bits
Can be detected by the last two carry out of the addition
BR register
Complementer and parallel adder
V
AC register
Overflow
AC: A register
BR: B register
Left most bit in AC and BR represent the sign of the numbers
Two sign bits are added or subtracted together with the other bits in the complementer and parallel adder
Overflow flip-flop V is set to 1 if there is an overflow, output carry is discarded in this case
In the addition of two unsigned number an overflow is detected from the end carry. In case of signed number sign bit is treated as part of number and so end carry does not indicate overflow
Minuend in AC
Subtrahend in BR
ACAC+BR′+1
V  Overflow
END
Augend in AC
Addend in BR
Add operation
Subtract operation
ACAC+BR
V  Overflow
END
Adds AC and 2’s complement of BR
Overflow must be checked because two numbers added could have the same sign
In case of overflow there is an erroneous result in AC
Sum = AC+BR including their sign bits
V=1 if XOR of the last two carries is 1 otherwise it is cleared to 0
Two sign bits (As, Bs) are added/subtracted together with the other bits
2’s complement of BR change its sign and so there is a chance of overflow
during subtraction and AC contains wrong result

## Slide 13
If multiplier bit is 1, copy multiplicand after shifting one bit left
Else copy 0 after 1 bit left shifting
Add the partial products
Hardware implementation for sign magnitude data
Adder for adding the partial products and store the result of multiplication in a register
Instead of shifting multiplicand towards left, partial product can be shifted towards right
Store multiplier in Q register and sign of multiplier in Qs
Store multiplicand in B register and sign of multiplier in Bs
SC = number of bits in multiplier initially, decrement by 1 after forming each partial product, process stops when SC is 0
 |  |  |  | 1 | 0 | 1 | 1 | 1 | Multiplicand
 |  |  |  | 1 | 0 | 0 | 1 | 1 | Multiplier
 |  |  |  | 1 | 0 | 1 | 1 | 1 | Partial product
 |  |  | 1 | 0 | 1 | 1 | 1 |  | Partial product
 |  | 0 | 0 | 0 | 0 | 0 |  |  | Partial product
 | 0 | 0 | 0 | 0 | 0 |  |  |  | Partial product
1 | 0 | 1 | 1 | 1 |  |  |  |  | Partial product
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | Sum of partial product
Multiplication algorithm
B register
A register
Complementer and parallel adder
Sequence counter (SC)
Bs
As
0
E
Qn
Q register
Qs

## Slide 14
Multiplicand in B
Multiplier in Q
=0
≠0
As  QsBs
Qs  QsBs
A  0, E  0
SC  n
Qn
EAA+B
Shr EAQ
SC SC-1
SC
END
Product is in AQ
=0
=1
Multiplicand B = 10111, Multiplier Q = 10011 |  |  |  | 
Operation | E | A | Q | SC
Initialization | 0 | 00000 | 10011 | 101
Qn = 1, add B | 0 | 00000 10111 10111 | 10011 | 
1st partial product | 0 | 10111 | 10011 | 
Shr EAQ | 0 | 01011 | 11001 | 100
Qn=1, add B | 0 0 1 | 01011 10111 00010 | 11001 | 
2nd partial product | 1 | 00010 | 11001 | 
Shr EAQ | 0 | 10001 | 01100 | 011
Qn=0, shr EAQ | 0 | 01000 | 10110 | 010
Qn=0, shr EAQ | 0 | 00100 | 01011 | 001
Qn=1, add B | 0 | 00100 10111 11011 | 01011 | 
Shr EAQ | 0 | 01101 | 10101 | 000
Right shift to place Qn-1 to Qn

## Slide 15
Booth’s multiplication algorithm
Speed up the multiplication process
Multiply binary integers in signed 2’s complement representation
String of 0’s in the multiplier require no addition but just shifting
A string of 1’s in the multiplier from bit weight 2k to weight 2m can be treated as 2k+1-2m
Example: 001110 = +14 has a string of 1’s from 23 to 21, k=3 and m=1. So +14 can be represented as 2k+1-2m = 24-21 = 14
Multiplication
M=multiplicand and +14 = Multiplier
M x 14 can be done as M x 24 – M x 21
Product can be obtained by shifting the binary multiplicand M four times towards left and subtracting M after shifting left by 1 bit
BR register
AC register
Complementer and parallel adder
Sequence counter (SC)
Qn
QR register
Qn+1
Hardware implementation
Qn: LSB of multiplier in QR
Qn+1: extra FF
Multiplicand in BR
Multiplier in QR
00
≠0
AC  0 Qn+1  0 SC  n
QnQn+1
ACAC+BR
ashr (AC and QR)
SC SC-1
SC
END
=0
ACAC+BR′+1
Multiply
11
10
01

## Slide 16
Multiplicand in BR
Multiplier in QR
00
≠0
AC  0 Qn+1  0 SC  n
QnQn+1
ACAC+BR
ashr (AC and QR)
SC SC-1
SC
END
=0
ACAC+BR′+1
Multiply
11
10
01
BR=10111 |  |  |  |  | 
QnQn+1 | BR′+1=01001 | AC | QR | Qn+1 | SC
 | Initialization | 00000 | 10011 | 0 | 101
10 | Subtract BR | 00000 01001 01001 |  |  | 
 | ashr | 00100 | 11001 | 1 | 100
11 | ashr | 00010 | 01100 | 1 | 011
01 | Add BR | 00010 10111 11001 |  |  | 
 | ashr | 11100 | 10110 | 0 | 010
00 | ashr | 11110 | 01011 | 0 | 001
10 | Subtract BR | 11110 01001 00111 |  |  | 
 | ashr | 00011 | 10101 | 1 | 000
Example: (-9) x (-13) = +117
Multiplicand in BR = -9 = 11001, 2’s complement of 11001 is 10111
Multiplier in QR = -13 = 11101, 2’s complement of 11101 is 10011

## Slide 17
Division algorithm: Division of two fixed-point binary numbers in signed magnitude representation is done
Divisor B consists of 5 bits, dividend A consists of 10 bits, five most significant bits (MSBs) of dividend are compared with the divisor
B = 10001, A = 01110 00000
Most significant 5 bits of A = 01110, less than divisor; so compare B and 6 MSBs of A
11010 | Quotient Q
10001)0111000000 011100 10001 | Dividend A 5 bits of A < B, so consider 6 bits of A Shift right B and subtract, enter 1 in Q
010110 10001 | 6 bits remainder > B Shift right B and subtract, enter 1 in Q
001010 00000 | Remainder < B, enter 0 in Q, shift right B
010100 10001 | Remainder >B Shift right B and subtract, enter 1 in Q
000110 00000 | Remainder <B, enter 0 in Q
110 | Final remainder
Sign of the result: Sign of quotient is determined from the sign of the dividend and the divisor. If the two signs are alike, sign of the quotient is plus. If they are unalike, sign is minus. The sign of the remainder is the same as the sign of the dividend.
Shift left
Add B′+1 to A
Is E=1
Qn  1
SC  SC-1
Qn  0
A  A+B
SC  SC-1
A≥B
yes
no
A<B
Is SC=0
yes
END
no
No change in dividend
as Qn = 0

## Slide 18
Example: Divisor B = 10001, B′+1 = 01111 |  |  |  | 
Operation | E | A | Q | SC
Dividend Shl EAQ Add B′+1 Set Qn = 1 as E=1 | 0 1 | 01110 11100 01111 01011 | 00000 00000 00001 | 101 100
Shl EAQ Add B′+1 Set Qn = 1 as E=1 | 0 1 | 10110 01111 00101 | 00010 00011 | 011
Shl EAQ Add B′+1 E = 0, Qn = 0 Add B Restore remainder | 0 0 1 | 01010 01111 11001 10001 01010 | 00110 00110 00110 | 010
Shl EAQ Add B′+1 Set Qn = 1 as E =1 | 0 1 | 10100 01111 00011 | 01100 01101 | 001
Shl EAQ Add B′+1 E=0, Qn=0 Add B Restore remainder | 0 0 1 | 00110 01111 10101 10001 00110 | 11010 11010 11010 | 000
E = end carry information about the relative magnitude of A and B
= 1 if A≥B and quotient, Qn = 1
= 0 if A<B and quotient Qn = 0, value of B is added to restore the partial
remainder in A to its previous value
Left shifting: Partial remainder is shifted towards left, quotient bits are also shifted, after 5 shifts quotient is in Q, remainder is in A
Divide overflow: Division operation may result in a quotient with an overflow
Consider a system with 5 bits registers. If 5 MSBs of A > B, size of the quotient becomes 6 bits, causes overflow, divide overflow flag (DVF) is set
Remainder
Quotient
Shift left
Add B′+1 to A
Is E=1
Qn  1
SC  SC-1
Qn  0
A  A+B
SC  SC-1
A≥B
yes
no
A<B
Is SC=0
yes
no
No change in dividend
as Qn = 0
END

## Slide 19
Qs=AsBs
SCn
EA A+B′+1
Divide operation
A≥B
E
EAA+B
DVF1
EAA+B
DVF0
End divide overflow
=0
=1
Shl EAQ
E
EA A+B′+1
A A+B′+1
E
EA A+B
Qn1
SC SC-1
SC
End
Dividend in AQ
Divisor in B
=0
≠0
=1
A≥B
=0
A<B
A≥B
=1
=0
Divide magnitudes
Example: Divisor B = 10001, B′+1 = 01111 |  |  |  | 
Operation | E | A | Q | SC
Initialization |  | 01110 | 00000 | 101
Shl EAQ E=0, add B′+1 E=1, Qn=1 | 0 1 | 11100 01111 01011 | 00000 00001 | 100
Shl EAQ E=0, add B′+1 E=1, Qn=1 | 0 1 | 10110 01111 00101 | 00010 00011 | 011
Shl EAQ E=0, add B′+1 E=0, add B | 0 0 1 | 01010 01111 11001 10001 01010 | 00110 00110 | 010
Shl EAQ E=0, add B′+1 E=1, Qn=1 | 0 1 | 10100 01111 00011 | 01100 01101 | 001
Shl EAQ E=0, add B′+1 E=0, add B | 0 1 | 00110 01111 10101 10001 00110 | 11010 11010 | 000
Remainder
Quotient
Dividend = 448
Divisor = 17
Quotient=26
Remainder = 6